PROFICIENCY TEST                                           GASOIL iis12G01EN 	2012

Report form A for analysis results of sample #12020

(according to the scope of EN590)

Report to: 	ing. R.J. Starink 						           before March 23th, 2012

fax.  + 31 181 69 4543 or email iisnl@sgs.com (preferred)

| Determination | Unit | Reference method (**) | Actual method used (**) | Unrounded result #12020 | result #12020 cfr. used standard |
| --- | --- | --- | --- | --- | --- |
| Ash content | %M/M | ISO6245 |  |  |  |
| Cetane Index |  | ISO4264 |  |  |  |
| Cloud Point | ºC | EN23015 |  |  |  |
| Cold Filter Plugging Point | ºC | EN116 |  |  |  |
| Carbon Residue on 10% res. | %M/M | ISO10370 |  |  |  |
| Copper corrosion 3hrs@50 oC | rating | ISO2160 |  |  |  |
| Density @ 15°C | kg/m3 | ISO12185 |  |  |  |
| FAME content | % V/V | EN14078 |  |  |  |
| Flash Point PMcc | °C | ISO2719 |  |  |  |
| Kinematic viscosity @40°C | mm2/s | ISO3104 |  |  |  |
| Lubricity by HFRR @60°C | µm | ISO12156 |  |  |  |
| Nitrogen, total | mg/kg | D4629 |  |  |  |
| Poly-aromatic hydrocarbons 1) | % M/M | EN12916 |  |  |  |
| Pour Point – manual | °C | ISO3016 |  |  |  |
| Pour Point – automated | ºC | D5950 |  |  |  |
| Sulphur content | mg/kg | ISO20846 |  |  |  |
| Total acid number | mgKOH/g | D974 |  |  |  |
| Water content | mg/kg | ISO12937 |  |  |  |

(**) Please see the letter of instructions

1)  Definition from EN12916:

%Poly Aromatic Hydrocarbons = sum of %di- and %tri+-Aromatic Hydrocarbons

Name of laboratory:	Date of sample receipt:

Country:                                                                                        City:

Name of contact person:                                                                       Date of report:

PROFICIENCY TEST                                           GASOIL iis12G01EN	2012

Report form B for analysis results of sample #12020

(according to the scope of EN590)

Report to: 	ing. R.J. Starink 							  before March 23th, 2012

fax.  + 31 181 69 4543 or email iisnl@sgs.com (preferred)

| Determination | unit | Reference method (**) | Actual method used (**) | Unrounded result #12020 | result #12020 cfr. used standard |
| --- | --- | --- | --- | --- | --- |
| Distillation at 760 mmHg | Manual or Automated mode ? : |  | A / M 1) |
| IBP | °C | ISO3405 |  |  |  |
| 10% recovered | °C | ISO3405 |  |  |  |
| 50% recovered | °C | ISO3405 |  |  |  |
| 90% recovered | °C | ISO3405 |  |  |  |
| 95% recovered | ºC | ISO3405 |  |  |  |
| FBP | °C | ISO3405 |  |  |  |
| %Volume at 250ºC | %V/V | ISO3405 |  |  |  |
| %Volume at 350ºC | %V/V | ISO3405 |  |  |  |
| % residue | %V/V | ISO3405 |  |  |  |

1) please circle the correct option

(**) Please see the letter of instructions

Name of laboratory:	Date of sample receipt:

Country:                                                                                        City:

Name of contact person:                                                                       Date of report:

# Instructions to participants for the Interlaboratory Study GASOIL iis12G01EN

*	Please confirm sample receipt as soon as you have received and checked the contents of this package, preferably using the fax form that you receive together with this package. Please complete the form and send it to i.i.s. (faxno. ++ 31 181 694543 or email iisnl@sgs.com). When the bottles have been broken, please do not accept the package from the courier. Please be noticed that we will only send replacement bottles at our cost when there is proof of the sample being broken upon receipt. This means that the consignee must report a broken bottle immediately. The consignee should take pictures of how the package and bottles looked upon arrival. We need these pictures to claim costs from the forwarders. The consignee should always mark any damage (dents, rips, leakage etc.) on the outside of the packages on the consignment note from the courier when it is delivered. Even minor damages should be reported. Please send copies of consignment notes and the pictures via email to nl.spijkenisse.saman@sgs.com.

*	Please record the date that the samples were received on report forms A and B.

*	This interlaboratory study concerns 2 identical samples Gasoil (1L bottle and ½ L bottle of sample #12020) Please treat the samples as if they were routine samples.

*	Each laboratory is requested to analyse the samples in the way it would normally do in day-to-day circumstances. Furthermore, each laboratory is advised to perform only those analyses you routinely do (but you are allowed to do all analyses if you like). It might be wise to start with those tests which are most important to your laboratory, especially if the supplied sample amount seems to be critical.

*	Report the analytical results using the indicated units on the report form. Report in the last column the analytical results, rounded in accordance with the standard method that was used. Report in the first result column the same analytical results but less rounded (we suggest to report one extra significant figure) in order to give more meaningful statistical calculations. For example, when you use ISO3104 for the determination of viscosity and you found a result of 3.14567 mm2/s, we request you to report 3.146 mm2/s in accordance with ISO3104 and 3.1457 mm2/s as ‘unrounded’ result.

*	Please report the methods used on the report form. If no Standard method is used, report 'in house' method or report the official standard method on which it is based with the remark 'mod' (modified).

# Also please report whether flash point was performed manually or by the use of an automated apparatus and by the use of electric or flame modes. Distillation was performed manually or by the use of an automated apparatus.

# *	On report form A and B an extra column is added on request of several participants.

# This column is named:”reference method”. In this column the method is mentioned, which the Institute for Interlaboratory Studies will use for calculating the z-scores. It is of utmost importance to know that the method, which is mentioned, is NOT mandatory.

So when you normally use in day-to-day circumstances an other method than the method prescribed in the ”reference method” column, please use your method and note the actual used method in the ”actual method used” column.

*	Please return the completed report forms to the Institute for Interlaboratory Studies in Spijkenisse, The Netherlands, preferably one week after sample receipt, but in any case before the indicated closing date:  MARCH 23, 2012 (preferably by email).

*	If you have any remarks/questions please contact:

ing. R.J. Starink, Institute for Interlaboratory Studies

P.O. box 200, NL-3200 AE Spijkenisse, The Netherlands

tel.no. + 31 181 694541

fax.no. + 31 181 694543

e-mail: iisnl@sgs.com