Instructions to participants for the Liquefied Butane Round Robin iis15S02B

*	Please confirm sample receipt as soon as you have received and checked the contents of this package, preferably using the fax form that you receive together with this package. Please complete the form and fax it to iis (email iisnl@sgs.com or faxno. + 31 181 694543).  If the package was visually damaged, please do not accept the package from the courier. Please note that we will only send replacement cylinder at our cost when there is proof of the cylinder is damaged upon receipt. This means that the consignee must report the damage immediately. The consignee should take pictures of how the package and cylinder looked upon arrival. We need these pictures to claim costs from the forwarders. The consignee should always mark any damage (dents, rips, leakage etc.) on the outside of the packages on the consignment note from the courier when it is delivered. Even minor damages should be reported. Please send copies of consignment notes and the pictures via email to nl.saman.iis@sgs.com.

*	This interlaboratory study concerns 1 sample of liquefied Butane (1 L cylinder, labelled #15086).  Please treat the sample as if it was a routine sample. The cylinder has a DIN-1 connection. Please notify us immediately in case you are not able to use this connection due to lack of a suitable connector. The DIN-1 connection is not included with the sample cylinder.

*	The valve on this cylinder is a dual port valve with dip tube. You must connect your DIN 1 fitting to the “Liquid” side of the valve indicated by the arrow, mentioned on the valve.  The hand wheel to operate the valve is already connected to the “Liquid” side of the valve.  The dip tube will only sample liquid if the cylinder is in the upright position (with the valve on the top).  The cylinder is not completely filled with liquefied butane, but does contain approximately 200 grams of liquid with approximately 5 bar helium over pressure. This is sufficient liquid for analysis but please be careful not to use the entire sample for purging your system.

*	Please record the cylinder number (the 6-digit (M) number on the back of the plasticized label and on the cylinder) and the weight of the cylinder (by receipt before opening the valve) on the report form.

*	On the report form an extra column is added on request of several participants. This column is named:”reference method”. In this column the method is mentioned, which the Institute for Interlaboratory Studies will use for calculating the z-scores. It is of utmost importance to know that the method, which is mentioned, is NOT mandatory. So when you normally use in day-to-day circumstances another method than the method prescribed in the ”reference method” column, please use your method and note the actual used method in the ”actual method used” column.

*	Report the analytical results using the indicated units on the report form. Report in the last column the analytical results, rounded in accordance with the standard method that was used. Report in the first result column the same analytical results but less rounded (we suggest to report one extra significant figure) in order to give more meaningful statistical calculations. For example, when you use D2163 for the determination of iso-Butane and you found a result of 76.816 %mol/mol, we request you to report 76.82 %mol/mol in accordance with ISO6974 and 76.816 %mol/mol as ‘unrounded’ result.

*	In order to avoid mix-up of test results we have added a box for your laboratory code. Please understand that it is not mandatory to use, but it will facilitate identification of your test results.

* 	 Preferably, please use our entry results website www.kpmd.co.uk/sgs-iis for reporting. In case you do not have internet or are reporting results after the closing date, it is however still possible to use the Word report form (incl. instructions) that was sent to all participants upon the start of the round. This completed Word document can be mailed or faxed to us.

* 	Please return the completed report forms to the Institute for Interlaboratory Studies in Spijkenisse, The Netherlands, preferably one week after sample receipt, but in any case before the indicated closing date:

JUNE 26, 2015 (preferably via website reporting).

*	If you have any remarks/questions please contact:

ing. R.J. Starink, Institute for Interlaboratory Studies

P.O. box 200, NL-3200 AE Spijkenisse, the Netherlands

tel.no. + 31 181 694541, fax.no. + 31 181 694543

e-mail: iisnl@sgs.com, 	website: www.iisnl.com